## Slide 1: Understanding Electricity-Theft Behavior via Multi-Source Data
Paper ID: 2086
Wenjie Hu, Yang Yang, Jianbo Wang, Xuanwen Huang and Ziqiang Cheng
Zhejiang University State Grid Power Supply Co. Ltd.

## Slide 2: Background
Electricity theft is a common illegal behavior in developing countries.
  In 2012, GDP in India was reported to drop 1.5% as a result of electricity theft[1];
  Uttar Pradesh lost 36% of its total electric power caused by electricity theft.
[1] PR Newswire. 2017. 96 Billion Is Lost Every Year To Electricity Theft: Utilities increasingly investing in solutions to combat theft and non-technical losses.
How does the power suppliers detect
electricity theft?

## Slide 3: Background
Hardware-driven Methods[2]:
  upgrade the meter structures;
  install a centralized;
  fully closed meter box.
Drawbacks:
  require expert domain knowledge;
  hard to design a general structure, due to the various pilfering tactics;
  effectiveness loss once thieves change their tactics.
[2] Li-Cai Guo, Zhi-Wei Peng, and Qiang Fan. 2010. A survey of electric energy metering and countermeasures to electric power stealing [J]. High Voltage Apparatus 46, 5 (2010), 86–88.

## Slide 4: Background
Data-driven Methods[3, 4]:
  analyze electricity usage records of each user
  analyze NTL[5] records
    Non-Technical Loss (NTL): the energy that is distributed but not billed
    Statistics are generally made in units of area (e.g., community, village, etc.)
Drawbacks:
  heavy burden for artificial analysis due to the massive data
  few labels for model learning
  isolated model and fail to obtain good performance
[3] ZibinZheng,YataoYang,XiangdongNiu,Hong-NingDai,andYurenZhou.2017. Wide and deep convolutional neural networks for electricity-theft detection to secure smart grids. IEEE Transactions on Industrial Informatics,
[4] SomaShekaraSreenadhReddyDepuru,LingfengWang,andVijayDevabhaktuni. 2011. Support vector machine based data classification for detection of electricity theft. In Power Systems Conference and Exposition (PES). IEEE, 1–8.
[5] Abhishek Chauhan and Saurabh Rajvanshi. 2013. Non-technical losses in power system: A review. In International Conference on Power, Energy and Control (ICPEC). IEEE, 558–561.
Goal: Identify electricity-theives via multi-source data in a hierarchical view.

## Slide 5: Hierarchical Structure of Power Grid Data
Data：(~2 years, from June 2017 to April 2019)
310,786 electricity usage records of user,
3,908 NTL records of transformer areas,
11 weather records of prefecture-level cities.
Macro-level:
Meso-level:
Micro-level:
1.45%
How does these information reveal
electricity-theft behaviors together?

## Slide 6: Observation in Micro-Level (User)
when the thief was caught
Different pricing electricity (wiki: https://en.wikipedia.org/wiki/Electricity_pricing)
Normal
users
Thieves
Usage variations before and after on-site checking：
The weather gets cooler from Jul. to Oct.
2. Normal users consume less power and perform stable
The slope of normal user tends to be negative, while half of thieves have a positive one
1. Significant increment after being caught

## Slide 7: Observation in Meso-Level (Area)
when the thief was caught
1. The less usage, the higher the NTL
2. After on-site checking, the NTL became stable.
Normal users perform stable and regular
Usage increases and NTL drops after being caught, indicating that NTL is a signal for electricity theft

## Slide 8: Observation in Macro-Level (Climate)
Statistics: the number of electricity thieves in each month
The correlations between temperature and total electricity usage
Summer
Winter
Climatic conditions would influence the user behavior of electricity usage (e.g., the usage of the air conditioner, heaters, etc.) and lead people to pilfer electricity.
Increased electricity with the high temperature
Increased electricity with the low temperature
Temperature is able to guide user behaviors of electricity usage

## Slide 9: Observation in Macro-Level (Climate)
Wasserstein distance
The gap between thieves and normal users is larger under extremely high or low temperatures
1. The scatterplot of electricity thieves seems disordered and irregular
2. The scatterplot of normal users is well fitted to a specific quadratic curve

## Slide 10: HEBR: Hierarchical Electricity-theft Behavior Recognition
Electricity usage records
NTL records
Temperature records
Macro-level:
Meso-level:
Micro-level:
HEBR aims to bridge the information from different sources and capture their hierarchical correlations when detecting electricity theft.
Estimate

## Slide 11: HEBR: Hierarchical Electricity-theft Behavior Recognition
model the influence from macro/meso to micro info.
uniform the influence from macro and meso level.
estimate the probability of electricity theft.
HEBR contains three levels of feature extraction and hierarchical fusion

## Slide 12
Recurrent and Fusion Layers
Current input
Latent recurrent representation in the k-th level
Temporal attention coefficient
HEBR: Hierarchical Electricity-theft Behavior Recognition

## Slide 13
Multi-step fusion mechanism
Temporal attention highlight the significance of the fused information at different time step
HEBR: Hierarchical Electricity-theft Behavior Recognition

## Slide 14
Formulation and Learning
Binary cross-entropy loss:
HEBR: Hierarchical Electricity-theft Behavior Recognition

## Slide 15: Experiments
Baseline methods
Handcrafted features

## Slide 16: Experiments
Baseline methods
Handcrafted features
Time Series classification[1][2] [3] [4]
Neural Networks [6][7] [8]
HEBR(Our approach)
[1] Donald J and James C. 1994. Using dynamic time warping to find
patterns in time series. SIGKDD (1994)
[2] Gustavo EAPA B, Xiaoyue W, and Eamonn J K 2011. A complexityinvariant
distance measure for time series. SDM (2011
[3] Thanawin R and Eamonn K. 2013. Fast shapelets: A scalable algorithm for discovering time series shapelets. ICDM (2013)
[4] Houtao D, George R, Eugene T, and Martyanov V 2013. A time series forest for classification and feature extraction. Information Sciences 239 (2013)
[5] Alex G, Abdelrahman M, and Geoffrey E H. [n.d.]. Speech recognition with deep recurrent neural networks. International Conference on Acoustics, Speech, and Signal Processing (ICASSP)
[6] Alex G, Abdelrahman M, and Geoffrey E H. [n.d.]. Speech recognition with deep recurrent neural networks. (ICASSP)
[7] Yong D, Wei W, and Liang W. 2015. Hierarchical recurrent neural network for skeleton based action recognition. In Proceedings of the IEEE conference
on computer vision and pattern recognition
[8] Zibin Z Yatao Y, Xiangdong N, Hong-Ning D, and Yuren Z 2017. Wide and deep convolutional neural networks for electricity-theft detection to secure smart grids. IEEE Transactions on Industrial Informatics 14, 4 (2017)

## Slide 17: Experiments
F0.5:
precision is more important than recall to real application
Variation: the stability of the model also needs to be considered

## Slide 18: Experiments

## Slide 19: Effectiveness Validation
Several ablation studies are conducted to validate the model effectiveness
Effect of multi-source information
Effect of fusion and attention operators

## Slide 20: Real World Application
Our work has been applied by State Grid of China to successfully catch electricity thieves in Hangzhou with a precision of 15%
when the thief was caught
e: electricity consumption of user
l: non-technical loss
c: climate(temperature)
: the attention scores of e and c (level 1)
: the attention scores of e and l (level 1)
: the attention scores of ec and el (level 2)

## Slide 21: Real World Application
Our work has been applied by State Grid of China to successfully catch electricity thieves in Hangzhou with a precision of 15%
when the thief was caught

## Slide 22: Conclusions
Analyze electricity-theft behaviors from three distinct levels of information based on multi-source data.
Propose the Hierarchical Electricity-theft Behavior Recognition (HEBR) model based on observational studies, which identifies electricity theft by fusing different levels of information, and validate its effectiveness using a real-world dataset.
Apply HEBR to catch electricity thieves on-site and achieve significant performance improvements.
Thanks! Q&A
More relevant research of our group: yangy.org
Contact: yangya@zju.edu.cn